# RE56 Labs
Specification document model – DELIVER 10 pages AT MAXIMUM

STUDENTS
DERRINGER ALINE
INACIO DAVID
GHNASSIA CLÉMENT

WORK SUBJECT
# HO: HANDOVER AND SELECTION/RESELECTION IN GSM/UMTS

DOCUMENT VERSION
Add a line for each new version you send
20/14/2014:	Modify Chapter:*

TEACHER COMMENTS
Date:
Comments:

---------------------------------------

1. PURPOSE OF THE SYSTEM FUNCTION (10 lines)

The handover and selection/reselection functionalities are needed to ensure mobility of users. Indeed, when a user move and change location, the network must be able to update the selected cell so the user does not lost the network and stay with a good connection. Handover and selection/reselection cover around the same needs but are used in different circumstances.

Selection is needed when the mobile has to select its first cell. It means that it's not currently connected to any network (the user switched it on or the network was lost because a lack of coverage). Reselection is used when the mobile is already connected and either idle or in packet switching (data transmission).

Handover is needed when the mobile user is currently used in circuit switching (classic voice call). Handover can be inter-system or intra-system. It is qualified by soft or hard depending on the conditions.

2. INPUT DATA AND PARAMETERS
- is_calling a boolean indicating if the user is trying to make a call (in circuit switcing)
- hysteresis_umts : a number to define an hysteresis between two umts signal strength. Avoid flapping scenarii.
- hysteresis_gsm : a number to define an hysteresis between two gsm signal strengths. Avoid flapping scenarii
- ntimes : a number indicating how many times the check has to be done before performing the operation (handover or reselection). Avoid flapping scenarii.
- update_strength(cell(s)) : Update the strength of the cells given in parameters at the mobile location.
- measure_landscape(type) is a function that returns the cells of desired type(UMTS or GSM) which have been detected at mobile location.

3. DESCRIPTION OF FORMULA AND ALGORITHM
(If your subject involves formulas, explain them in this section. Label and explain the variables used.)

Free space propagation Friis formula
Calculate the power received at the mobile from an antenna depending on distance and frequency used

Pr = Pe + Ge + Gr – (32,44 + 20 log(F) + 20log(d))

Pr = Power received at the mobile (in dBm)
Pe = Power emitted by the base station (in dBm)
Ge = Gain at base station in (dBi)
Gr = Gain at mobile station in (dBi)
F = Frequency of the used wave (in MHz)
d = Distance between the mobile and the base station (in km)

(Describe the algorithm used. The description should not be in a computer language but in the form of a pseudo-code: « In programming, the pseudo-code is a way to describe an algorithm without reference to a particular programming language. The writing pseudo-code can often take well to the extent of the difficulty of implementing the algorithm, and develop a structured approach in its construction. (Wikipédia) ». Diagrams can be used too.)

function selectionUMTS
input
List<Cell> candidate_set
output
Cell selected
body
for cell in candidate_set do
if cell.strength >= cell.minimum_strength && ! cell.is_barred then
selected ← cell
break
end if
end do
end body
end function

function selectionGSM
input
List<Cell> candidate_set
output
Cell selected
body
candidate_set.sort('desc')
for cell in candidate_set do
if cell.strength >= cell.minimum_strength && ! cell.is_barred then
selected ← cell
end if
end do
end body
end function

function reselectionUMTS
input
Cell selected
List<Cell> candidate_set
hysteresis
ntimes
output
Cell selected
body
candidate_set.sort('desc')
for cell in candidate_set do
if ! cell.is_barred then
if selected.type equals 'GSM' then
if cell.strength > cell.minimum_strength then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
else	// selected.type equals 'UMTS'
if cell.strength > cell.minimum_strength && cell.strength - selected.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
end if
break
end if
end do
end body
end function

//we assume that entering to this function means that there is no UMTS //cell available
function reselectionGSM
input
Cell selected
List<Cell> candidate_set
hysteresis
output
Cell selected
body
candidate_set.sort('desc')
for cell in candidate_set do
if ! cell.is_barred then
if selected.type equals 'GSM' then
if cell.strength > cell.minimum_strength && cell.strength - selected.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
else	// selected.type equals 'UMTS'
if cell.strength > cell.minimum_strength
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals cell.ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
end if
end if
end do
end body
end function

function handoverUMTS
input
List<Cell> active_set
List<Cell> neighbor_set
hysteresis
ntimes
output
List<Cell> active_set
List<Cell> neighbor_set
body
//we first get the best cell inside the active set
for cell in active_set do
maxActive ← max(active_set)
if cell.strength > cell.minimum_strength and maxActive.strength - cell.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
active_set.remove(cell)
neighbor_cell.add(cell)
end if
else
cell.ntimes ← 0
end if
end do

neighbor_set.sort('desc')
for cell in neighbor_set do
if active_set.length < active_maxlength then
if active_set.length equals 0 then
maxActive ← 0
else
maxActive ← max(active_set)
end if

if cell.strength > cell.minimum_strength and cell.strength - maxActive.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
neighbor_cell.remove(cell)
active_set.add(cell)
end if
else
cell.ntimes ← 0
end if
else
break
end if
end do

for i ← 0 ; i < neighbor_set.length ; i ← i + 1 do
minActive ← min(active_set)
maxNeighbor ← max(neighbor_set)
if maxNeighbor.strength - minActive.strength > hysteresis then
maxNeighbor.ntimes ← maxNeighbor.ntimes + 1
if maxNeighbor.ntimes equals ntimes then
active_set.replace(minActive, maxNeighbor)
neighbor_set.replace(maxNeighbor, minActive)
end if
else
maxNeighbor.ntimes ← 0
end if
end do
end body
end function

function handoverGSM
input
Cell primary
List<Cell> neighbor_set
hysteresis
ntimes
output
Cell primary
List<Cell> neighbor_set
body
for cell in neighbor_set do
if cell.strength > cell.minimum_strength
if primary is null then
cell.ntimes ← cell.ntimes + 1
else if cell.strength - primary.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
else
cell.ntimes ← 0
end if

if cell.ntimes equals ntimes then
if primary is not null then
neighbor_set.add(primary)
end if
neighbor_set.remove(cell)
primary <- cell
end if
else
cell.ntimes ← 0
end if
end do
end body
end function

function main
input
boolean is_calling
int hysteresis_umts
int hysteresis_gsm
int ntimes
body
Cell selected
Cell primary
List<Cell> active_set
neighbor_umts_set
neighbor_gsm_set
boolean is_update_calling ← false

while 1 do
update_strength(selected)
update_strength(primary)
update_strength(active_set)
update_strength(neighbor_umts_set)
update_strength(neighbor_gsm_set)

if primary is null and active_set.length equals 0 then //selection

candidate_set ← measure_landscape('UMTS')
selected ← selectionUMTS(candidate_set)
if selected is null then
candidate_set ← measure_landscape('GSM')
selected ← selectionGSM(candidate_set)
end if

if selected is not null then
neighbors_umts_set ← selected.getNeighborsUMTS()
neighbors_gsm_set ← selected.getNeighborsGSM()
end if
else
if is_calling then
if not is_update_calling then
if selected.type equals 'UMTS'
active_set.add(selected)
else
primary ← selected
end if
is_update_calling ← true
end if

if primary equals null and active_set.length equals 0 then

is_calling ← false
else
handoverUMTS(active_set, neighbor_umts_set, hysteresis_umts, ntimes)
if active_set.length() equals 0 then
handoverGSM(primary, neighbor_gsm_set, hysteresis_gsm, ntimes)
end if
end if

else
is_update_calling ← false
active_set.empty()
primary ← null
selected ← reselectionUMTS(selected, neighbor_umts_set, hysteresis_umts, ntimes)
if selected.type equals 'GSM' || selected.strength < selected.minimum_strength then
selected ← reselectionGSM(selected, neighbor_gsm_set, hysteresis_gsm, ntimes)
end if
end if
end if
sleep(500)	//wait for 0.5 sec
end do
end body
end function

4.OUTPUT DATA
(Describe the list of output data of the function. What are the results of the simulation?)

The main function should simulate the operations that the mobile or network must take depending on the situation. The function performs simulation of selection/reselection on GSM and UMTS, soft handover (UMTS to UMTS) and hard handover (UMTS to GSM, GSM to UMTS, and GSM to GSM).

The selected cell is only used when the user is not calling. When the user gives a call, the content of the selected cell is inserted wether in the active_set list (if the selected cell is UMTS) or in the primary variable (if the selected cell is GSM).

5. VALIDATION ON ONE EXAMPLE
(Describe one hand-made example of the algorithm steps. The purpose of this exercise is to verify the accuracy of your work. Take a reduced set of data to describe the inputs, the calculations made, and the outputs obtained.)

6. BIBLIOGRAPHY USED
(Describe the list all the references you found to your project: title, author, year of publication, website, etc.)

- UMTS, services, architectures et WCDMA, Javier Sanchez and Mamadou Thioune, Hermes
- Réseaux mobiles, Sami Tabbane, Hermes
- Simulating soft handover and power control for enhanced umts, V. Vassiliou, J. Antoniou, A. Pitsillides, and G. Hadjipollas, Department of Computer Science in University of Cyprus