# RE56 Labs
Specification document model – DELIVER 10 pages AT MAXIMUM

STUDENTS

DERRINGER ALINE
INACIO DAVID
GHNASSIA CLÉMENT

WORK SUBJECT
HO: HANDOVER AND SELECTION/RESELECTION IN GSM/UMTS

DOCUMENT VERSION

04/23/2014:	First version of the document
05/14/2014:	Second version of the document

TEACHER COMMENTS

Date:
Comments:

---------------------------------------

# PURPOSE OF THE SYSTEM FUNCTION

The handover and selection/reselection functionalities are needed to ensure mobility of users. Indeed, when a user move and change location, the network must be able to update the selected cell so the user does not lost the network and stay with a good connection. Handover and selection/reselection cover around the same needs but are used in different circumstances.

Selection is needed when the mobile has to select its first cell. It means that it's not currently connected to any network (the user switched it on or the network has been lost because a lack of coverage). Reselection is used when the mobile is already connected and either idle or in packet switching (data transmission). Although the term reselection is used for both of the cases, reselection in idle mode and reselection in data transmission are different mecanisms and use differents algorithms.

Handover is needed when the mobile user is currently used in circuit switching (classic voice call). Handover can be inter-system or intra-system. It is qualified by soft or hard depending on the conditions.
Idle mode
UMTS		GSM
		No service cell selected	Service cell selection
Service cell selection	Service cell reselection	Selection using C1 criteria	Reselection using C2 criteria

Connected mode
Data transmission		Voice call
UMTS	GPRS/EDGE	UMTS	GSM
Reselection using the active set and monitored set with RSSI* and RXLEV parameters	Reselection using C'1, C31 and C32 criteria. Also based on RXQUAL measurement	Handover using the active set and monitored set with RXLEV parameters	Handover using C1 and C2 criteria

# INPUT DATA AND PARAMETERS

- is_calling a boolean indicating if the user is trying to make a call (in circuit switcing)
- hysteresis_umts : a number to define an hysteresis between two umts signal strength. Avoid flapping scenarii.
- hysteresis_gsm : a number to define an hysteresis between two gsm signal strengths. Avoid flapping scenarii
- ntimes : a number indicating how many times the check has to be done before performing the operation (handover or reselection). Avoid flapping scenarii.
- update_strength(cell(s)) : Update the strength of the cells given in parameters at the mobile location.
- measure_landscape(type) is a function that returns the cells of desired type(UMTS or GSM) which have been detected at mobile location.

# DESCRIPTION OF FORMULA AND ALGORITHM

## Free space propagation Friis formula

Calculate the power received at the mobile from an antenna depending on distance and frequency used

Pr = Pe + Ge + Gr – (32,44 + 20 log(F) + 20nlog(d))

Pr = Power received at the mobile (in dBm)
Pe = Power emitted by the base station (in dBm)
Ge = Gain at base station in (dBi)
Gr = Gain at mobile station in (dBi)
F = Frequency of the used wave (in MHz)
d = Distance between the mobile and the base station (in km)
n = Diffraction factor

## SINR calculation

Give the signal interference ratio at the mobile for an antenna depending on the others signals received at this location

SINR(a) = Pr(a) / ∑(Pr(other signals))

SINR(a) = Signal interference ratio at the mobile for signal a
Pr(a) = Power received at the mobile for signal a in Watt
∑(Pr(other signals))= Sum of all signals except signal a which are received at the mobile location (in Watt)

## Algorithms
### Cell selection and reselection in idle mode (valid for GSM, not sure for other systems)
Selection and reselection in idle mode consists of having the best fitted cell selected when the mobile station (MS) moves and change cell. Selection enable the MS to select the best suitable cell. To perform the reselection mechanism, the mobile station do measurements of the BCCH (Broadcast Control Channel) signals and keep the 6 strongest carriers based on their signal strength.
In order to determine which cell is the best fitted for the selection and reselection, we use C1 or C2 parameters. For selection, we do calculate the best cell with C1 parameter. For reselection we use C1 and C2 parameters based on the 6 best neighbors (provided by the current selected cell)
C1 is used as a minimum signal level criterion for cell reselection. The pass loss criterion is satisfied if C1 is positive. It is computed as below:
C1 = AV_RXLEV – RX_ACCESS_MIN
AV_RXLEV: average RSSI received at the mobile (in dBm), during a certain time. C1 must be positive to connect
RX_ACCESS_MIN: minimum RXLEV necessary to be allowed to select the cell. This is a cell dependent parameter.
Please notice that if the regarded cell is not in the same location area (LA) as the current selected cell, we will provide the C1 calculation with a negative offset. The reason for this is that changing LA require changing location update (LU) procedure that consumes network signaling capacity. The C1 formula becomes in this case:
C1 = AV_RXLEV – RX_ACCESS_MIN – CELL_RESELECT_HYSTERESIS
CELL_RESELECT_HYSTERESIS is a parameter given by the BCCH
The C2 criterion is used for cell ranking in the GSM cell reselection process. Because we have hierarchical cell structures with micro-cells as well as larger cells covering the same areas, we improve the C1 parameter for micro-cells. This mechanism will avoid for a mobile station moving fast to get attached in micro-cell instead of a larger cell.
if T < PENALTY_TIME then
C2 = C1 + CELL_RESELECT_OFFSET – TEMPORARY_OFFSET
else
C2 = C1 + CELL_RESELECT_OFFSET
end if
T is a timer which is triggered when the regarded cell is entering the 6 best candidate cells for reselection.
CELL_RESELECT_OFFSET is a parameter that is used to prioritize one cell in relation to the others
PENALTY_TIME and TEMPORARY_OFFSET are given by the BCCH. This is used to penalize the cell when its just enters the list of the strongest carriers.
CELL_RESELECT_PARAM_IND inform the MS about which reselection criterion (C1 or C2) is used in the cell. It is broadcast on the BCCH.
/*Below is the selection mechanism
1. We do measurements of the 6 best cells detected based on their signal carrier strengths.
2. We calculate C1 parameter for each of one based on informations provided by their BCCH
3. We ask for selection to the cell.
#### */ Not sure of that before
#### Procedure for (C1, C2)
1. mobile compute C1 and C2 values for the serving cell and the neighbor cells at least every 5 seconds.
2. A cell-selection is triggered if one of the following events occurs:
- the pass loss criterium has become too high (C1 < 0)
- the serving cell has become barred
- downlink signaling failure is experienced
- a neighbor cell has C2 higher than the serving cell for a period of 5 seconds. If LA of the neighbor cell is not the same as L1 of the serving cell, C2 of neighbor cell must exceed C2 of serving cell for at least CELL_RESELECT_HYSTERESIS [for 5 seconds ?]. If a reselection occurred in the last 15 seconds, the C2 value of the neighbor cell must exceed C2 value for the serving cell by at least 5dB for 5 seconds
- a random access attempt is still unsuccessful after Max retrans repetition, Max retrans being a parameter broadcast on the control channel

### Cell handover for GSM
Handover is performed the MS is in dedicated mode. Handover is decided by the network based on the MS measurements and the antenna measurements as well. Multiples causes for handover are defined.
#### Measurements
In order to take the decision of handover, measurements both by the mobile station (which are transmitted to the network) and by the base transceiver station are needed.
##### Measurements by the MS
###### Bit Error Rate
###### Quality of reception: RXCALL
RXQUAL is a value between 0 and 7 where each value corresponds to an estimated number of bits errors in a number of bursts. Greater is RXQUAL, Greater is the Bit Error Rate (and worse it the connection).
RXQUAL	Bit Error Rate (BER)
0	BER < 0.2 %
1	0.2 % < BER < 0.4 %
2	0.4 % <= BER < 0.8 %
3	0.8 % <= BER < 1.6. %
4	1.6 % <= BER < 3.2 %
5	3.2 % <= BER < 6.4 %
6	6.4% <= BER < 12.8 %
7	12.8 % <= BER

###### Received level: RXLEV
###### Received level from neighbors cells: RXLEV_NCELL(n)
The neighbor cells are transmitted by the current cell.
##### Measurements by the BTS
###### Quality of reception: RXCALL
The same as for the MS, but regarding the uplink
###### Received level: RXLEV
The same as for the MS, but regarding the uplink.
Distance between MS and BTS: MS_BS_DIST
Evaluated with Timing Advance.
Interference level
Measured in unallocated time slots.
#### Handover decision
Based on the measurements taken by the MS and the BTS, the decision of handover is taken following theses rules
##### Quality is too low i.e. RXQUAL is too high (in uplink or downlink)
RXQUAL_UL > L_RXQUAL_UL_H or RXQUAL_DL > L_RXQUAL_DL_H
##### Received level (RXLEV) is too low (in uplink or downlink)
RXLEV_UL < L_RXLEV_UL_H or RXLEV_DL < R_RXLEV_DL_H
##### Distance between MS and BTS is too large (usually > 35 km)
MS_BS_DIST > MS_RANGE_MAX
##### A neighbor cell is more favorable
RXLEV_NCELL(n) > RXLEV_MIN(n) and RXLEV_NCELL(n) - RXLEV_DL > HO_MARGIN
As we have seen in reselection, we can use a timer to prevent a fast moving mobile phone to connect to micro-cell where a larger cell is available. We replace HO_MARGIN by HO_MARGIN_TIME as above
If T < DELAY_TIME then
HO_MARGIN_TIME = HO_MARGIN(n) + HO_STATIC_OFFSET(n)
Else
HO_MARGIN_TIME(n) = HO_MARGIN(n) + HO_STATIC_OFFSET(n) - HO_DYNAMIC_OFFSET(n)
End if
#### Result
Eventually, we can provide the mechanism which is presented and based on the explaining below
 If RXLEV too low then
intercell HO due to level
 Else if MS_BS_DIST is too large
intercell HO due to distance
 Else if a neighbor cell is more favorable
intercell HO due to power budget
 Else if RXQUAL is too high
intracell HO due to quality
 End if

When a handover is decided, we also need to change to the best cell. Actually, the same mechanisms as we have seen for reselection are available to execute a handover toward a right cell.

### Cell reselection (in idle ?) mode for GPRS (Edge)
The pass loss criterion C'1 is used as a minimum signal level criterion for GPRS cell reselection.
C'1 = RXLEV – GPRS_RXLEV_ACCESS_MIN
GPRS_RXLEV_ACCESS_MIN is provided by the BCCH of the regarded cell.

The signal level threshold criterion parameter C31 for hierarchical cell structure (HCS) is used to determine whether prioritize hierarchical GPRS cell reselection applies.
C31(serv) = RXLEV(serv) – HCS_THR(serv)

if PRIORITY_CLASS(neigh) equals PRIORITY_CLASS(serv) then
C31(neigh) = RXLEV(neigh) – HCS_THR(neigh)
else
if T < GPRS_PENALTY_TIME then
C31(neigh) = RXLEV(neigh) – HCS_THR(neigh) – GPRS_TEMPORARY_OFFSET
else
C31(neigh) = RXLEV(neigh) – HCS_THR(neigh)
end if
end if

PRIORITY_CLASS gives cells different priory depending on their characteristics (pico-cell, micro-cell, macro-cell, ...)
HCS_THR is the signal threshold for applying HCS GPRS reselection
GPRS_PENALTY_TIME give a duration for which the temporary offset GPRS_TEMPORARY_OFFSET is applied. T is a timer that is started from 0 at the time the cell inters in the list of strongest carriers.

The cell-ranking criterion parameter (C32) is used to select cells among those with the same priority and is defined for the serving cell and the neighbor cells
C32(serv) = C'1(serv)

if PRIORITY_CLASS(neigh) equals PRIORITY_CLASS(serv) then
if T < GPRS_PENALTY_TIME then
C32(neigh) = C1(neigh) + GRPS_RESELECT_OFFSET(neigh) – GPRS_TEMPORARY_OFFSET
else
C32(neigh) = C1(neigh) + GPRS_RESELECT_OFFSET(neigh)
end if
else
C32(neigh) = C1(neigh) + GPRS_RESELECT_OFFSET(neigh)

As well as for C1 criterion, the parameter GPRS_CELL_RESELECT_HYSTERESIS cab be substracted from the C32 criteria of the neighbor cells. This hysteresis is also substracted from C31 criterion if requested by network.

When the neighbor cell does not belong to the same area location (LA) as the serving cell, RA_RESELECT_HYSTERESIS is substracted from the C32 criterion of the neighbor cell.

In case cell selection occurred within the previous 15 seconds, all neighbor cells are penalized by 5dB in oder to avoid ping-pong between cells.

#### Procedure for (C'1, C31, C32)
1. Mobile computes the values for C'1, C31, C32 criteria for the serving cell and the nonserving cells at least every second. A cell reselection is then triggered if one of the following events occurs:
- The pass criterion parameter C'1 indicate that the pass loss to the cell has become too high (C'1 < 0)
- A nonserving suitable cell is evaluated to be better than the serving cell. The best cell is the cell with the highest C32 value among
- the cells that have the highest priority class among the cell that fulfill C31 >= 0
- all cells, if no cell fulfill the criterion C31 >= 0
- Downlink signaling failure is experienced
- The cell on which the mobile is camping has become barred
- A random access attempt is still unsuccessful adter MAX_RESTRANS_RATE
attempt.
Notice that the cell on which the mobile was camped on must not be returned to within 5 seconds
### UMTS measurements
#### Received Signal Code Power (RSCP)
That is the power level the pilot channel of a cell is received and usually expressed in dBm. With this parameter, difference cells using the same carrier can be compared and handover or cell reselection can be taken
#### Received Signal Strength Indication (RSSI)
That's the signal power over the complete 5MHz carrier which includes all components received, including the signals from the current and neighboring cells on the same frequency.
#### Signal Interference Noise Ratio (Ec/No)
This is the received energy per chip (Ec) of the pilot channel divided by the total noise power density (No). In other words, the Ec/No is the RSCP divided by the RSSI.
The better this value is, the better can a signal of a cell be distinguished from all overall noise. That is the indicator we use as the SINR (Signal to Interference Noise Ratio) for UMTS measurements.

function update_strength
input
List<Cell> cell_set
mobile
output
List<Cell> cell_set
body
distance ← 0
for cell in cell_set do
distance ← sqrt(pow(abs(mobile.x – cell.x),2) + pow(abs(mobile.y – cell.y), 2))
cell.strength ← cell.signal + cell.gain + mobile.gain – (32,44 + 20log(cell.frequency) + 20log(distance))
end do
end body
end function

function selectionUMTS
input
List<Cell> candidate_set
output
Cell selected
body
for cell in candidate_set do
if cell.strength >= cell.minimum_strength && ! cell.is_barred then
selected ← cell
break
end if
end do
end body
end function

function selectionGSM
input
List<Cell> candidate_set
output
Cell selected
body
candidate_set.sort('desc')
for cell in candidate_set do
if cell.strength >= cell.minimum_strength && ! cell.is_barred then
selected ← cell
end if
end do
end body
end function

function reselectionUMTS
input
Cell selected
List<Cell> candidate_set
hysteresis
ntimes
output
Cell selected
body
candidate_set.sort('desc')
for cell in candidate_set do
if ! cell.is_barred then
if selected.type equals 'GSM' then
if cell.strength > cell.minimum_strength then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
else	// selected.type equals 'UMTS'
if cell.strength > cell.minimum_strength && cell.strength - selected.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
end if
break
end if
end do
end body
end function

//we assume that entering to this function means that there is no UMTS //cell available
function reselectionGSM
input
Cell selected
List<Cell> candidate_set
hysteresis
output
Cell selected
body
candidate_set.sort('desc')
for cell in candidate_set do
if ! cell.is_barred then
if selected.type equals 'GSM' then
if cell.strength > cell.minimum_strength && cell.strength - selected.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
else	// selected.type equals 'UMTS'
if cell.strength > cell.minimum_strength
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals cell.ntimes then
selected ← cell
end if
else
cell.ntimes ← 0
end if
end if
end if
end do
end body
end function

function handoverUMTS
input
List<Cell> active_set
List<Cell> neighbor_set
hysteresis
ntimes
output
List<Cell> active_set
List<Cell> neighbor_set
body
for cell in active_set do
maxActive ← max(active_set)
if cell.strength < cell.minimum_strength then
active_set.remove(cell)
neighbor_cell.add(cell)
else if maxActive.strength - cell.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
active_set.remove(cell)
neighbor_cell.add(cell)
end if
else
cell.ntimes ← 0
end if
end do

neighbor_set.sort('desc')
for cell in neighbor_set do
if active_set.length < active_maxlength then
if active_set.length equals 0 then
maxActive ← 0
else
maxActive ← max(active_set)
end if

if cell.strength > cell.minimum_strength and cell.strength - maxActive.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
if cell.ntimes equals ntimes then
neighbor_cell.remove(cell)
active_set.add(cell)
end if
else
cell.ntimes ← 0
end if
else
break
end if
end do

isSwitched ← true
while isSwitched do
minActive ← min(active_set)
maxNeighbor ← max(neighbor_set)
if maxNeighbor.strength - minActive.strength > hysteresis then
maxNeighbor.ntimes ← maxNeighbor.ntimes + 1
if maxNeighbor.ntimes equals ntimes then
active_set.replace(minActive, maxNeighbor)
neighbor_set.replace(maxNeighbor, minActive)
end if
else
maxNeighbor.ntimes ← 0
isSwitched ← false
end if
end do
end body
end function

function handoverGSM
input
Cell primary
List<Cell> neighbor_set
hysteresis
ntimes
isHandoverNeeded
output
Cell primary
List<Cell> neighbor_set
body
neighbor_set.sort('desc')
for cell in neighbor_set do
if not cell.is_barred && cell.strength > cell.minimum_strength
if primary is null then
cell.ntimes ← cell.ntimes + 1
else if cell.strength - primary.strength > hysteresis then
cell.ntimes ← cell.ntimes + 1
else
cell.ntimes ← 0
end if

if cell.ntimes greater than ntimes and isHandoverNeeded then
primary ← cell
end if
else
cell.ntimes ← 0
end if
end do
end body
end function

function main
input
boolean is_calling
int hysteresis_umts
int hysteresis_gsm
int ntimes
body
Cell selected
Cell primary
List<Cell> active_set
neighbor_umts_set
neighbor_gsm_set
boolean is_update_calling ← false

while 1 do
update_strength(selected)
update_strength(primary)
update_strength(active_set)
update_strength(neighbor_umts_set)
update_strength(neighbor_gsm_set)

if selected is null then //selection

candidate_set ← measure_landscape('UMTS')
selected ← selectionUMTS(candidate_set)
if selected is null then
candidate_set ← measure_landscape('GSM')
selected ← selectionGSM(candidate_set)
end if

if selected is not null then
neighbors_umts_set ← selected.getNeighborsUMTS()
neighbors_gsm_set ← selected.getNeighborsGSM()
end if
else
if is_calling then
if not is_update_calling then
if selected.type equals 'UMTS'
active_set.add(selected)
else
primary ← selected
end if
is_update_calling ← true
end if

if primary equals null and active_set.length equals 0 then
is_calling ← false
else
handoverUMTS(active_set, neighbor_umts_set, hysteresis_umts, ntimes)

handoverGSM(primary, neighbor_gsm_set, hysteresis_gsm, ntimes, active_set.length equals 0)

if active_set.length > 0 and selected is not max(active_set)
primary ← null
tmp_selected ← max(active_set)

else if selected is not primary then
tmp_selected ← primary
end if

if tmp_selected not equals selected then
selected ← tmp_selected
neighbors_umts_set ← selected.getNeighborsUMTS().minus(active_set)
neighbors_gsm_set ← selected.getNeighborsGSM()
end if
end if

else
if is_update_calling then
is_update_calling ← false
if not active_set.is_empty() then
active_set.empty()
else
primary ← null
end if
end if
Cell tmp_selected
tmp_selected ← reselectionUMTS(selected, neighbor_umts_set, hysteresis_umts, ntimes)
if tmp_selected.type is null then
tmp_selected ← reselectionGSM(selected, neighbor_gsm_set, hysteresis_gsm, ntimes)
end if
if tmp_selected not equals selected then
selected ← tmp_selected
neighbors_umts_set ← selected.getNeighborsUMTS()
neighbors_gsm_set ← selected.getNeighborsGSM()
end if
end if
end if
sleep(500)	//wait for 0.5 sec
end do
end body
end function

4.OUTPUT DATA

The main function should simulate the operations that the mobile or network must take depending on the situation. The function performs simulation of selection/reselection on GSM and UMTS, soft handover (UMTS to UMTS) and hard handover (UMTS to GSM, GSM to UMTS, and GSM to GSM).

The selected cell is only used when the user is not calling. When the user gives a call, the content of the selected cell is inserted either in the active_set list (if the selected cell is UMTS) or in the primary variable (if the selected cell is GSM).

5. VALIDATION ON ONE EXAMPLE

For the example we are going to take following parameters:

is_calling ← false
hysteresis_umts ← 4
hysteresis_gsm ← 2
ntimes ← 3

At the beginning all the sets are empty and the variables primary and selected are null, so we enter in the first condition in the main function.

We now invoke the measure_landscape with UMTS parameters. This function simply return a set of detected UMTS cells associated with their signal strengthes depending on the distance between each cells and the mobile phone. Let's suppose that the function return the following measures:

candidate_set ← {Cell1: 5, Cell2: 11, Cell3: 15}

Now, in order to select an appropriate cell, we invoke selectionUMTS function passing the candidate_set. If we suppose that the minimum_strength needed to select the cell is 10 and no one is barred, the function will return the first cell with a strength greater or equal than the minimum strength required. In this case, the cell returned is Cell2, with type UMTS. From this cell (cell(2)), we retrieve the neighbors (in UMTS and GSM). Let's suppose we have:

selected ← (Cell2: 11)
neighbor_umts_set ← {Cell3, Cell 4, Cell6}
neighbor_gsm_set ← {Cell11, Cell12}

In the next iteration in the loop. We implement measurement of the neighbor cells as well as the selected cell. We assume that we get the following measures:

selected ← (Cell2: 11)
neighbor_umts_set ← {Cell3: 15, Cell 4:18, Cell6:8}
neighbor_gsm_set ← {Cell11:18, Cell12:16}

Since we have a selected cell, we enter in the else statement. We are going to invoke the function reselectionUMTS(). For a reselection is being performed, the cell must be stable, which means that it has to match the conditions during three loops. We suppose that the values don't move during three loops, so the cell Cell4 will be the result of reselection. Indeed, the strength of Cell4 is greater or equal than Cell1 added with hysteresis for UMTS. Because we changed cell, the neighbor sets changed as well. We get from the reselected cell the following values and their associated strength (after we proceeded to measurements):

selected ← (Cell4: 18)
neighbor_umts_set ← {Cell2: 11, Cell3:15, Cell6:8}
neighbor_gsm_set ← {Cell11:15, Cell16:8}

Let's imagine that we want to give a call. First of all, if the cell is a UMTS cell, it's added in the active_set. Let's suppose we have now the following values:

selected ← (Cell4: 18)
active_set ← {Cell4: 18}
neighbor_umts_set ← {Cell2: 11, Cell3:22, Cell6:8}

Notice: Meanwhile, the neighbor_gsm_set is updated (the ntime is incremented for possible candidate), in case of interruption with UMTS connection.

If the results measurements are not changing for three loops. Now we retrieve the neighbors from the cell in the active set which has the maximum strength. The results will be eventually:

active_set ← {Cell4: 18, Cell3:22}
neighbor_umts_set ← {Cell5: 11, Cell6:8}
neighbor_gsm_set ← {Cell12:14, Cell13:18}

And if the measurements are not changing for more three loops, the Cell4 will be removed from the active set and added in the neighbor set; the selected cell is now referencing the Cell3 (because it is in the max strength in the active_set.

selected ← (Cell3: 22)
active_set ← {Cell3:22}
neighbor_umts_set ← {Cell4: 18, Cell5:11, Cell6:8}

Now, if the mobile is moving and all the UMTS's cells have a strength lower than the minimum required (10); a hard handover towards GSM cell is needed. We assume that the Cell13 has already a “ntimes” greater than the “ntimes” required to be qualified as stable (don't forget that the handoverGSM treatment has been performed since we are in a call).

selected ← (Cell3: 9)
active_set ← {Cell3:9}
neighbor_umts_set ← {Cell2: 8, Cell4: 7, Cell6:9}
neighbor_gsm_set ← {Cell12:14, Cell13:18}

After the iteration in the loop, we performed hard handover and retrieve neighbors of the new primary cell.

selected ← (Cell13: 18)
primary ← { Cell13: 18}
active_set ← {}
neighbor_umts_set ← {Cell9: 9}
neighbor_gsm_set ← {Cell12:14, Cell19:8}

The communication is stopped, we juste remove the primary and optionnally empty the active_set (which in this case was already empty since the communication was under GSM).

selected ← (Cell13: 18)
primary ← {}
active_set ← {}
neighbor_umts_set ← {Cell9: 9}
neighbor_gsm_set ← {Cell12:14, Cell19:8}

Because the mobile is now idle, the algorithm will return to selection/reselection mode.

6. BIBLIOGRAPHY USED

- UMTS, services, architectures et WCDMA, Javier Sanchez and Mamadou Thioune, Hermes
- Réseaux mobiles, Sami Tabbane, Hermes
- Simulating soft handover and power control for enhanced umts, V. Vassiliou, J. Antoniou, A. Pitsillides, and G. Hadjipollas, Department of Computer Science in University of Cyprus