# RE56 Labs
Specification document model – DELIVER 10 pages AT MAXIMUM

STUDENTS
DERRINGER ALINE
INACIO DAVID
GHNASSIA CLÉMENT

WORK SUBJECT
# HO: HANDOVER AND SELECTION/RESELECTION IN GSM/UMTS

DOCUMENT VERSION
Add a line for each new version you send
20/14/2014:	Modify Chapter:*

TEACHER COMMENTS
Date:
Comments:

---------------------------------------

1. PURPOSE OF THE SYSTEM FUNCTION (10 lines)

The handover and selection/reselection functionalities are needed to ensure mobility of users. Indeed, when a user move and change location, the network must be able to update the selected cell so the user does not lost the network and stay with a good connection. Handover and selection/reselection cover around the same needs but are used in different circumstances.

Selection is needed when the mobile has to select its first cell. It means that it's not currently connected to any network (the user switched it on or the network was lost because a lack of coverage). Reselection is used when the mobile is already connected and either idle or in packet switching (data transmission).

Handover is needed when the mobile user is currently used in circuit switching (classic voice call). Handover can be inter-system or intra-system. It is qualified by soft or hard depending on the conditions.

2. INPUT DATA AND PARAMETERS
(Describe the list of data and parameters required to perform the function)

3. DESCRIPTION OF FORMULA AND ALGORITHM
(If your subject involves formulas, explain them in this section. Label and explain the variables used.)

Free space propagation Friis formula
Calculate the power received at the mobile from an antenna depending on distance and frequency used

Pr = Pe + Ge + Gr – (32,44 + 20 log(F) + 20log(d))

Pr = Power received at the mobile (in dBm)
Pe = Power emitted by the base station (in dBm)
Ge = Gain at base station in (dBi)
Gr = Gain at mobile station in (dBi)
F = Frequency of the used wave (in MHz)
d = Distance between the mobile and the base station (in km)

(Describe the algorithm used. The description should not be in a computer language but in the form of a pseudo-code: « In programming, the pseudo-code is a way to describe an algorithm without reference to a particular programming language. The writing pseudo-code can often take well to the extent of the difficulty of implementing the algorithm, and develop a structured approach in its construction. (Wikipédia) ». Diagrams can be used too.)

function selectionUMTS
input
int frequency	//carrier signal frequency for UMTS
output
Cell selectedCell	//selected Cell at the end of algorithm
body
candidateCell ← null
do
candidateCell = getUMTSCells(frequency)	// we found
if (candidateCell is not null || (candidateCell.strength >= candidateCell.minimumSelectionStrength)) && (not candidateCell.isBarred) then
//we are allowed to use this cell
selectedCell ← candidateCell
end if
while candidateCell is not null
end body
end function

function selectionGSM
input
int frequency	//carrier signal frequency for UMTS
output
Cell selectedCell	//selectedCell at the end of algorithm
body
List<Cell> candidateCells ← []
Cell tmpCell ← null
do
tmpCell ← getUMTSCells(frequency)	//we found a potential cell
if (tmpCell is not null || (tmpCell.strength >= tmpCell.minimumSelectionStrength)) && (! tmpCell.isBarred) then
//this is a valid Cell
candidateCells.add(tmpCell)
end if
while tmpCell is not null

//now we find the best cell
if candidateCells.length > 0 then
Cell tmpCell
for tmpCell in candidateCells do
if selectedCell is null || tmpCell.strength > selectedCell.strength) then
selectedCell ← tmpCell
end if
end do
end if
end body
end function

function reselectionUMTS
input
List<Cell> neighborCells	//list of UMTS neighbor cells
selectedCell	//cell that is currently selected
output
selectedCell	//new selectedCell
body
//first we get the best neighbor cell
candidateCell ← null
if neighborCells.length > 0 then
Cell tmpCell
for tmpCell in neighborCells do
if (candidateCell is null || (tmpCell.strength > candidateCell.strength)) && (not tmpCell.isBarred) then
candidateCell ← tmpCell
end if
end do
end if

//now we check if we need to reselect (or not)
if candidate is not null && (candidateCell.strength > candidateCell.minimumReselectionStrength) then
//if we are currenlty in GSM
if selectedCell.type equals 'GSM' then
selectedCell ← candidateCell
else	//selectedCell.type equals 'UTMS'
if candidateCell.strength - selectedCell.strength > candidateCell.deltaReselection then
selectedCell ← candidateCell
end if
end if
end if
end body
end function

function reselectionGSM
input
List<Cell> neighborCells	//list of GSM neighbor cells
selectedCell	//cell that is currently selected
output
selectedCell	//new selectedCell
body
//first we ge best neighbor cell
candidateCell ← null
if neighborCells.length > 0 then
Cell tmpCell
for tmpCell in neighborCells do
if (candidateCell == null || tmpCell.strength > candidateCell.strength) && (! tmpCell.isBarred) then
candidateCell ← tmpCell
end if
end do
end if

//now we check if we need to reselect or not
if candidate is not null && (candidateCell.strength > candidateCell.minimumReselectionStrength) then
if selectedCell.type equals 'GSM' then
if candidateCell.strength - selectedCell.strength > candidateCell.deltaReselection then
selectedCell ← candidateCell
end if
end if
else //selectedCell.type equals 'UTMS'
//if the strength of the current UMTS cell is below a defined threshold and the strength of candidate GSM cell is aboce defined threshold
if(selectedCell.strength - selectedCell.minimumStrength < selectedCell.deltaReselectionToGSM) && (candidateCell.strength - candidateCell.minimumStrength > candidateCell.deltaReselectionFromUMTS then
selectedCell ← candidtateCell
end if
end if
end if
end body
end function

function mobile
body
while(true) do
//we are not calling; we use selection/reselection
if not this.isCalling then
//we are not connected; we try to select
if this.selectedCell is null then
this.selectedCell ← reselectionUMTS(this.frequencyUMTS)
if this.selectedCell is null then
this.selectedCell ← reselectionGSM(this.frequencyGSM)
end if
else	//we are already connected; let's use reselection
reselectedCell ← reselectionUMTS(this.selectedCell, this.frequencyUMTS)
//if we indeed did reselection, so no need to try reselection towards GSM (optimization)
if reselectedCell equals this.selectedCell then
this.selectedCell ← reselectionGSM(this.selectedCell, this.frequencyGSM)
else
this.selectedCell ← reselectedCell
end if
end if
end if
sleep(500) //wait for 0.5 seconds
end do
body
end function

4.OUTPUT DATA
(Describe the list of output data of the function. What are the results of the simulation?)

5. VALIDATION ON ONE EXAMPLE
(Describe one hand-made example of the algorithm steps. The purpose of this exercise is to verify the accuracy of your work. Take a reduced set of data to describe the inputs, the calculations made, and the outputs obtained.)

6. BIBLIOGRAPHY USED
(Describe the list all the references you found to your project: title, author, year of publication, website, etc.)

- UMTS, services, architectures et WCDMA, Javier Sanchez and Mamadou Thioune, Hermes
- Réseaux mobiles, Sami Tabbane, Hermes